| Top and bottom frame, castors, adjustable feet. | Installing castors and adjustable feet. | Finish the assembly. |
| --- | --- | --- |
| Stand up the front and rear frame. | Inserting the end of the frame into the slots on the top and bottom frame. | Locking the screws |
| Locking the bottom frame, down-cable management. | Locking the top frame, up-cable management. | Installing the fan tray. |
| Finish the assembly. (Main frame, castors and adjustable feet.) | Horizontal mounting Rails. (Left and right each 3 pcs) | Installing horizontal mounting rails by screws. |
| Finish the assembly. | *Only for cabinet width 800 mm* (12 pcs in total of square connector) | *Only for cabinet width 800 mm* Installing the connector to horizontal mounting Rail by screws. |

| *Only for cabinet width 800 mm* Finish the assembly. | *Only for cabinet width 800 mm* Installing the 12 pieces of square connector. | 19’ Vertical Mounting Rail. ( 4 pcs in total) |
| --- | --- | --- |
| *Only for cabinet width 800 mm* Installing the Vertical Mounting Angle to Mounting Rail. (The middle part is connector) | *Only for cabinet width 800 mm* | Installing the plastic plug (door stop) on the front frame and rear frame. |
| Side panel. (Left side and Right side) | Installing side panels. | Plastic lock for side panel. |
| Locking plastic lock into the side panel. | Finish to assemble the side panels. | Front and Rear door. |
| Assemble the front and rear door. | Put the pin on the bottom plate, then use the hinge bolt to contact the bottom plate and front door. | The chart of assemble of drawer set step. |
| Attached the top section of front door. | Attached the top section of front door. | Attached the top section of front door. |
| Finish the rack assembly. | Exploded Drawing. |  |

| Sever rack Package CARTON A: |  |  |
| --- | --- | --- |
| Item | Qty | REMARK |
| TOP | 1 |  |
| BOTTOM | 1 |  |
| HORIZONTAL MOUNTING ANGEL | 6 |  |
| CABLE ENTRY COVER | 4 |  |
| CONNECTOR BOX | 12 | FOR 800 WIDTH CABINET |
| CASTOR | 4 |  |
| SCREW BAG | 1 |  |
| FAN TRAY UNIT | 1 |  |
| CATON B |  |  |
| Item | Qty | REMARK |
| FRAME | 2 |  |
| VERTICAL CABLE MANAGEMENT | 2 | FOR 800 WIDTH CABINET |
| VERTICAL MOUNTING PROFILE | 4 |  |
| CATON C |  |  |
| Item | Qty | REMARK |
| FRONT DOOR | 1 |  |
| REAR DOOR | 1 |  |
| SIDE PANEL | 2 |  |

The screw number would be adjusted in accordance with Cabinet Size

| Screws type | Pictures | Spec. | Q’ty | Usage |
| --- | --- | --- | --- | --- |
| Round head cross screw |  | M5*12 | 4 | *Latch of side panel: 4*1=4 |
| Hex Socket Screw |  | M8*12 | 16 | *Top cover: =8 screws *bottom plate: =8 screws |
| Round head cross screw |  | M6*12 | 66 (W:600mm) or 120 (W:800mm) | Mounting rail: 6pcs*8 screws=48 Castors：4*4 screws=16 Only Width 800mm rack: a. Vertical cable management : 2*6=12 screws+2*6=12 Nut b. Connective block (only Width 800mm rack): 4*12=48 screws |
| Round head cross self tapping |  | M4*8 | 12 | Top cover and bottom cover: 4 X 2 scrws=8 *Fan tray: 1X4=4 |
| Connected nut |  | M6 | 4+4 | *Ground connection |

# Text boxes

P03 Series Rack Assembly Guide